Syed Muhammad Irtaza Hyder
NS 378514

CN Assignment #2

Q) If your computed bandwidth is significantly lower (for a TCP Taho connection using 0.01% packet loss) than 10Gbps, you should consider using some other TCP variant for congestion control. Which TCP variant you will use in this situation? What is the maximum achievable bandwidth for the newly selected TCP variant under this arrangement (0.01% packet loss)?

TCP Variant:
TCP Cubic
Reason:
TCP Cubic is good for high-speed, long-distance networks due to its aggressive congestion window management, enabling efficient bandwidth utilization.
Compared to other modern approaches like BBR, Cubic offers a more standardized approach, while BBR emphasizes maintaining maximum throughput and minimizing latency, making it suitable for high-bandwidth connections with high packet loss to allow smoother performance.
On the other hand, Vegas focuses on latency-based congestion control, prioritizing low delay over maximum throughput, making it beneficial for real-time applications but less optimal for high-speed networks with long distances.

Maximum Bandwidth Calculation:

Where X = Bandwidth (bytes), s = packet size (bytes), R = round trip time (sec), p = packet event/loss rate, tRTO = TCP retransmission timeout (sec), b = number of packets acknowledged by single TCP ack.

Assuming maximum packet size:
s = maximum TCP packet size = 64Kb = 65,535 bytes. (https://stackoverflow.com/questions/2613734/maximum-packet-size-for-a-tcp-connection)

b = 1 for smallest denominator
p = 0.01/100 = 0.0001 (given)

tRTO = 3 seconds (https://support.microsoft.com/en-us/topic/how-to-modify-the-tcp-ip-maximum-retransmission-time-out-7ae0982a-4963-fa7e-ee79-ff6d0da73db8)

Assuming R ≈ 0s as transmission distance very small.

X = 1.189x10^(10) bytes ≈ 8 Gbps